## Slide 1
Team: first_wewillwin
Member: Jiacheng Lin1, Yulin Xiao1, Dong Zheng1,
Instructor:Wenjun Li1, Jun Liu1
1Hangzhou Dianzi University
28th April, 2025
WWW 2025 SmartMem Competition

## Slide 2
Introduction
Team member Introduction
Introduction to the Competition
Difficulty of the competition

## Slide 3
Team member Introduction: Lin Jiacheng, Xiao Yulin, Zheng Dong
Team member Introduction
  EDA basic commonality and cutting-edge technology research (optimization, synthesis, place and route, MBSE technology roadmap)
  JG-specific chip design simulation technology R&D (chip feature extraction, macro model, modeling tool development)
  Large language model training and agent design in the vertical field of RF/MMIC
Jiacheng Lin
Master's degree
Yulin Xiao
Master's degree
Dong Zheng
Master's degree
EDA Technology Innovation Center
Research Interests: AI and Big Data, Multi-modal Recognition, Image Segmentation

## Slide 4
Dynamic memory failure timing prediction
  Based on the memory and kernel log data of large-scale servers (with a total of hundreds of millions of logs and tens of thousands of servers), a machine learning model is trained to detect online whether a server will experience memory failure within the next 7 days. (Classification problem)
Introduction to the Competition
Data Introduction
Evaluation Index
3. System and Configuration Dimensions
manufacturer: Server manufacturer
model: CPU model
PN: DIMM part number
Capacity: DIMM capacity
memory_type: DIMM type (e.g., DDR4)
2. Error and Log Dimensions
Retryrderrlogparity: Retry read error log parity information
Retryrderrlog: Retry log, records error type and check (parity/ECC)
Burst_info: Memory DQ and burst error parity bits
Error_type: Error type (read or scrub/erase)
Log_time: Error occurrence timestamp
1. Hardware Dimensions
Cpuid: CPU ID
Channelid: Channel ID (each CPU has multiple channels)
Dimmid: DIMM ID (each channel connects multiple DIMMs)
Rankid: Rank ID (each DIMM has 1 or 2 Ranks)
Deviceid: Device ID (each DIMM has multiple devices)
Introduction to the Competition

## Slide 5
Difficulty of the competition
Task Difficulties
  Highly Imbalanced Data: Out of a total of 72,959 machines in the training data, only 673 experienced memory failures (0.9%).
  Difficult Feature Engineering: The vast majority of the original features are Categorical features.
  Key Constraint - Prediction Window:
  Predictions must occur before the actual failure alarm_time and need to meet specific lead time requirements. t_pred + 15 minutes <= alarm_time <= t_pred + 15 minutes + 7 days.
IMC 2
IMC 3
CPU 1
DIMM 0
DIMM 0
DIMM 0
DIMM 1
DIMM 1
DIMM 1
DIMM 1
DIMM 1
DIMM 1
DIMM 0
DIMM 0
DIMM 0
Channel 0
Channel 1
Channel 2
Channel 0
Channel 1
Channel 2
IMC 0
IMC 1
CPU 0
DIMM 0
DIMM 0
DIMM 0
DIMM 1
DIMM 1
DIMM 1
DIMM 1
DIMM 1
DIMM 1
DIMM 0
DIMM 0
DIMM 0
Channel 0
Channel 1
Channel 2
Channel 0
Channel 1
Channel 2
bank 0
bank 1
bank 14
bank 15
…
bank 0
bank 1
bank 14
bank 15
…
rank 0
rank 1
Difficulty of the competition

## Slide 6
Methodology
Feature Engineering
Multi-window Fusion

## Slide 7
Visual Charts
Feature Engineering
Observation window
Time
serial_number | ChannelId | rankid | bankid | row | col | LogTime | manufacturer | region
sn_1 | 2 | 1 | 2 | 129329 | 744 | 1705898605 | B | 0
sn_1 | 2 | 1 | 2 | 129329 | 744 | 1705898729 | B | 0
  Key Observation:
  The error distribution exhibits significant clustering rather than random scattering.
  There are clearly concentrated areas of row/column/regional errors.
  Error logs form a time series, requiring capture of dynamic patterns within sliding windows.
Machine Learning
Feature Engineering

## Slide 8
Statistical Features
(Window Aggregation)
Intra-Window Dynamic Features
(First Order/Change)
Label construction
Error Count & Types: Total logs & CE/SCRUB counts (Reflects Error Activity).
Underlying Error Severity: Total/Max Burst/DQ (Measures Error Severity).
Hardware Location Concentration (Nunique): Unique ID counts per level (Identifies Fault Localization)
Automated Fault Mode Recognition: Bank/Row/Cell level modes (Aids Diagnosis Type).
1. Error Frequency Change: Stats on time diffs between logs (Captures Frequency Fluctuation/Acceleration).
Error Severity Change Rate: Stats on Burst/DQ count diffs (Indicates Error Severity Deterioration).
Identifying Positive Sample Windows: The positive sample window preceding a failure is identified, with the window closest to the failure event labeled as 1.
Linear Decay: Starting from the window labeled as 1, we trace back in time, and for earlier feature windows, their label values decrease linearly, with the label linearly decaying to a minimum of 0.5.
Negative Sample Labels: All other feature windows that do not fall into the above positive sample windows (including all windows from SNs that never experienced a failure, and windows from failing SNs that are far removed in time from the failure event) are assigned a label of 0.
Statistical correlation characteristics
Label construction
Comparison and Testing
Internal Structure: Implemented through the development of a LightGBM model.
……
Feature Engineering
After testing on the dataset and continuously optimizing the features and parameters used by the model, as well as employing five-fold cross-validation, (stage 1 score: 0.21)
From logs to predictable signals
Comparison and Testing

## Slide 9
LGMB Model
多窗口
融合
Memory Address Log
MCE Log
Kernel Log
Stage 1(Machine Learnning):
Using a regression model, based on the information within a machine's specified window and historical log data, we determine the probability of the machine experiencing a failure within the next 7 days following that window.
Stage 2( Multi-window fusion Stage):
Further utilize the regression model to derive judgment results across multiple windows. Achieve the fusion of multi-perspective results across different sliding windows.
Serial Number | Fault Time
sn_32644 | 1722945465
sn_53527 | 1725607371
.... | ....
sn_65571 | 1723834531
Feature Engineering
Stage 0(Feature Engineering Stage): Real-time extraction of frequency statistics and principle-based features from logs to form the training/testing data.
Voting
Moudle
Multi-window Fusion

## Slide 10
Capture different scale patterns: Using multiple sliding Windows of different lengths (such as the 2727s, 2000s, 3600s you are using) is to attempt to capture event patterns at different time scales. Short Windows may capture sudden anomalies, while long Windows may capture slowly accumulating trends.
LGMB Model
Multi-window Fusion
Voting
Moudle
Sliding Windows2000S
Sliding Windows2727S
Sliding Windows3600S
Multi-window Fusion

## Slide 11
Experiments
Voting Model Design
Final Score Variation Results

## Slide 12
Voting Model Design
Phase 1: Candidate SN Screening:
Initially screen likely failing SNs. Calculate cumulative weighted votes per SN from base models. This significantly cuts candidate SNs (around 78% retention), focusing on higher-probability failures and filtering low-confidence predictions.
Phase 2: Timestamp Clustering and Voting:
Merge similar predictions and find initial failure time. Collect all models' predicted timestamps per SN, cluster them, select the highest-scoring cluster. The median timestamp of this best cluster is the SN's preliminary predicted time, fusing models and initially locating failure.
Phase 3: Timestamp Refinement:
Refine initial time using original model predictions. Using Phase 2's median time as a reference, find nearby predictions (within +/- 3600s) from all original models (used 93.1% of the time). If no nearby predictions exist, use a weighted average to calculate the final timestamp.
Correlation Analysis Chart
Voting Model Design

## Slide 13
Final Score Variation Results
Effectiveness of the Approach
Hybrid Correction of Multi-Time Phase and Multi-Model Strategies for Fund Prediction
Restructured Observation Window: Explored more potential first-order, second-order, statistically correlated, and trend-related features to improve model accuracy and correct baseline version prediction results.
Model Voting ResultsM: Increased model robustness through multi-window model fusion voting.
1
2
3
Restructured Feature Engineering: Rebuilt feature engineering, reformulating the labels for a regression task.
Experiment Strategies | Stage 1 Results
lgbm+3600s window | 0.188
lgbm+2727s window | 0.190
lgbm+2000s window | 0.186
Baseline prediction | NAN
Multi-window voting | 0.191
Score Trend of Different Strategies
Experiment Strategies | Stage 1 Results
lgbm+3600s window | 0.236
lgbm+2727s window | 0.251
lgbm+2000s window | 0.205
Baseline prediction | 0.207
Multi-window voting | 0.260
Improve 0.009 stage_1
Improve 0.001 stage_2
Improve 0.015 stage_1
Improve 0.002 stage_2
Improve0.019 stage_1
Final Score Variation Results

## Slide 14
Conclusions

## Slide 15
Attempted but ineffective approaches
Exploration and Outlook
Target Alignment Optimization: Optimize the labels/loss function to more directly align with the SN-level F1 metric.
Model Feature Deepening:
Model: Attempted multi-model ensembling/fusion.
Features: Refined/expanded features (cross-window, global).
External Information Fusion: Consider incorporating system-level information such as server load and temperature.
1
2
3
4
Validation Strategy Upgrade: Explore time-based cross-validation to better reflect real-world deployment scenarios.
Window Aggregation Features: The model heavily relies on window statistical features (count, Nunique, difference), without deeply exploring sequence models.
Core Feature Engineering: Focuses on bit-level analysis (burst/dq) and hardware-level Nunique (fault_mode), potentially with redundancy or insufficient interaction exploration.
1
2
3
4
Regression Label Exploration: Employed a [1.0, 0.5] linearly decaying label, but there is a disconnect between the regression target and the final SN-level F1 metric.
Static Sampling Strategy: Employed coarse file-level sampling with sample number limits, without attempting dynamic or hard sample mining.
Conclusions